## Slide 1
M.TECH REINFORCEMENT LEARNING • RESEARCH DEMONSTRATION
Methodology-Faithful Reconstruction and D₀ Sensitivity Analysis of Q-Learning-Based Routing in a 3D Wireless Sensor Network
Syeda Nishat Reva Academy for Corporate Excellence, Reva University, Bengaluru Guide / Mentor: J. B. Simha
Reference Paper: I. Jrhilifa, H. Ouadi, and A. Jilbab, “Q-learning-based Optimization of Smart Home's Wireless Sensors Network Lifetime,” International Journal of Renewable Energy Research, Vol. 13, No. 1, 2023.
Notes: Good [morning/afternoon]. My name is Syeda Nishat, and this is my M.Tech Reinforcement Learning project: a methodology-faithful reconstruction and D0 sensitivity analysis of a Q-learning-based routing scheme for 3D wireless sensor networks, based on the 2023 IJRER paper by Jrhilifa, Ouadi, and Jilbab. I want to be upfront from this first slide: this is a reconstruction of the published methodology, not an exact numerical replication, because the original topology and some simulation parameters were not available to me. Over the next few slides I will walk through the problem, the reconstructed methodology, my experimental results, how they compare with the published values, and an extension I added — a D0 sensitivity study.

## Slide 2
MOTIVATION
Background and the Routing Problem
1
Wireless Sensor Networks
Spatially distributed, battery-powered sensor nodes relay data toward a central sink node.
2
Energy-Constrained Nodes
Nodes run on finite batteries; recharging or replacement is often impractical in deployed settings.
3
Multi-Hop Routing
Data travels sensor-to-sensor before reaching the sink, so every hop consumes shared network energy.
4
Network Lifetime Problem
The goal is to balance energy use across nodes to maximize successful transmissions before nodes are exhausted.
Why Reinforcement Learning? Q-learning enables adaptive, next-hop routing decisions that jointly weigh residual energy, distance, and remaining hop count — without needing a full model of network dynamics.
M.Tech Reinforcement Learning • Q-Learning WSN Routing — Reconstruction & D0 Sensitivity
02
Notes: Let me set up the problem. Wireless sensor networks are made of many small, battery-powered nodes that must relay sensed data back to a sink, often over multiple hops. Because these nodes usually cannot be recharged easily, energy-aware routing is critical — the network 'lifetime' depends on how evenly and efficiently energy is spent. This is where reinforcement learning, specifically Q-learning, becomes attractive: it lets each routing decision adapt based on residual energy, distance, and hop count, learned online from reward signals, rather than relying on a fixed shortest-path rule like Dijkstra's algorithm.

## Slide 3
REFERENCE & OBJECTIVE
Reference Paper and Research Objective
REFERENCE PAPER
Q-learning-based Optimization of Smart Home's Wireless Sensors Network Lifetime
Authors: I. Jrhilifa, H. Ouadi, A. Jilbab Journal: Intl. Journal of Renewable Energy Research Volume / Year: Vol. 13, No. 1, 2023
Investigates a Q-learning-based energy-efficient routing scheme for a smart-home WSN and compares it against a Dijkstra shortest-path baseline.
MY RESEARCH OBJECTIVE
Reconstruct the methodology and experimentally validate the implementation.
Reconstruct the reward function, radio energy model, and propagation model
Implement and validate on a reconstructed 45-node, 3D deployment
Compare completed rounds and delivered data against published values
Extend the study with a D0 sensitivity analysis
⚠
This work is a methodology-faithful reconstruction, not an exact numerical replication, because the original topology / coordinate information and some implementation details were unavailable.
M.Tech Reinforcement Learning • Q-Learning WSN Routing — Reconstruction & D0 Sensitivity
03
Notes: This slide introduces the paper I am reconstructing: Jrhilifa, Ouadi and Jilbab, published in the International Journal of Renewable Energy Research in 2023. Their study proposes a Q-learning-based routing scheme for a smart-home WSN and benchmarks it against Dijkstra's shortest-path algorithm. My objective is not to copy their numbers, but to reconstruct their reward function, energy model, and propagation model faithfully, implement it end to end, and validate it experimentally. I want to stress the framing in the amber box: because I did not have access to the original node coordinates or full simulator configuration, this is a methodology-faithful reconstruction — not a claim of exact numerical replication. I will repeat this distinction throughout the presentation.

## Slide 4
METHODOLOGY
Reconstructed Methodology Workflow
1
45-node 3D WSN deployment
↓
2
Network construction
↓
3
Communication links
↓
4
Candidate routing paths
↓
5
Q-learning route evaluation
6
Energy feasibility check
↓
7
Q-value update
↓
8
Route selection
↓
9
Energy deduction
↓
10
Next transmission round
Cyclical process: steps 1–3 build the network once; steps 4–10 repeat every transmission round until no feasible route remains.
M.Tech Reinforcement Learning • Q-Learning WSN Routing — Reconstruction & D0 Sensitivity
04
Notes: This diagram shows the ten-step reconstructed methodology, from network setup all the way to executing a transmission round. First, we build the 45-node 3D network and its communication links, then generate candidate routing paths for each sensor. The highlighted blue boxes are the reinforcement-learning core: for every round, candidate routes are evaluated by Q-learning, checked for energy feasibility, and the Q-value is updated. A route is then selected, energy is deducted safely, and the process repeats for the next transmission round. This loop continues until the network can no longer find a feasible complete path — which, as I'll show later, is exactly how my experiment terminated.

## Slide 5
SYSTEM MODEL
System Model and Parameters
Parameter | Value | Provenance
Total nodes | 45 | Paper / reference setup
Sensor nodes | 44 | Paper / reference setup
Sink | 1 | Paper / reference setup
Deployment volume | 16 × 13 × 2.5 m | Paper / reference setup
Initial energy | 0.5 J / node | Paper / reference setup
Packet size | 512 bits | Paper / reference setup
E_elec | 5 × 10⁻⁸ J/bit | Radio energy model
E_amp | 1 × 10⁻¹⁰ J/bit/m² | Radio energy model
Coordinate seed | 42 | Our reconstruction
Communication range | 7.0 m | Our assumption
D₀ (propagation threshold) | 4.0 m | Our assumption
Max hops / max stored paths | 6 / 20 per source | Routing-table limit
Paper / reference
Assumed / reconstructed
Full provenance table (Table I) is reported in the paper.
M.Tech Reinforcement Learning • Q-Learning WSN Routing — Reconstruction & D0 Sensitivity
05
Notes: Here are the exact system parameters used in the reconstruction, taken directly from Table I of my paper. Green italic labels mark values taken directly from the reference paper or the standard radio energy model — 45 total nodes, 44 sensor nodes plus one sink, a 16 by 13 by 2.5 metre deployment volume, 0.5 joules of initial energy per node, and 512-bit packets. Amber italic labels mark values I had to assume because they weren't available in the original paper — the coordinate seed of 42, a 7-metre communication range, and a D0 propagation threshold of 4 metres. I want to be transparent about this distinction because it directly explains why my numerical results differ from the published ones.

## Slide 6
RL FORMULATION
Q-Learning and Energy Model
State
Action
Reward
Path Quality & Energy Feasibility feed the update below every routing decision.
Q-Value Update
Q_new = (1 − α) · Q_old + α · [Reward + PathQuality]
Reward Function
Reward = E_residual / (distance^β × hop_count)
Transmit Energy
E_TX(k,d) = E_elec · k + E_amp · k · d^β
β = 2 for d ≤ D₀ (free-space); β = 4 for d > D₀ (multipath)
Receive Energy
E_RX(k) = E_elec · k
M.Tech Reinforcement Learning • Q-Learning WSN Routing — Reconstruction & D0 Sensitivity
06
Notes: This slide covers the reinforcement-learning core and the radio energy model. On the left is the state-action-reward loop: at each decision point, the agent observes the network state, selects a candidate next-hop action, and receives a reward. On the right, the Q-value update rule blends the old Q-value with alpha times the sum of reward and path quality — path quality captures residual energy and remaining hop count of candidate nodes. The reward itself is the candidate node's residual energy divided by the propagation-weighted distance and hop count. For energy, I use the standard first-order radio model: transmit energy has an electronics term plus an amplifier term that scales with distance raised to the power beta, and beta itself switches between 2 and 4 depending on whether the link distance is below or above the threshold D0 — this is the free-space versus multipath transition, and it's exactly the parameter I later study in the sensitivity analysis.

## Slide 7
IMPLEMENTATION
Implementation and Validation
✓
Python
✓
NetworkX
✓
Q-Learning Routing Engine
✓
Radio Energy Model
✓
Route Feasibility Checker
✓
Link-Level Energy Audit
✓
Executed Jupyter Notebook
✓
GitHub Repository
✔
The implementation was independently tested against manually calculated link-level energy values — every audited transmit/receive energy value agreed with the manual calculation to the displayed numerical precision.
Validation layers performed:
Single-packet reward / Q-value / energy audit
Link-by-link TX/RX energy audit (6 links)
Controlled infeasible-route rejection test
Full 45-node lifetime experiment
M.Tech Reinforcement Learning • Q-Learning WSN Routing — Reconstruction & D0 Sensitivity
07
Notes: To move from methodology to a working system, I implemented everything in Python using NetworkX for the graph structure, with a dedicated Q-learning routing engine, the radio energy model, and a route-feasibility checker. Everything ran in an executed Jupyter notebook, version-controlled in a GitHub repository for reproducibility. Critically, I didn't just trust the code — I independently hand-calculated transmit and receive energy for a six-link path and compared it against the implementation's output. As shown in the green box, every value matched to the displayed precision. I also ran a controlled test where a node was deliberately given too little energy to confirm that infeasible routes are correctly rejected before they can be selected.

## Slide 8
FULL-NETWORK EXPERIMENT
Final 45-Node Experiment Results
9,189
Completed Rounds
4,704.77
Kbits Transmitted
4.080833 J
Energy Consumed
17.919167 J
Final Residual Energy
44 / 0
Alive / Dead Nodes
Chart: Residual Energy Variation (Fig. 1)
| 0 | 2000 | 4000 | 6000 | 9189
Total Residual Energy (J) | 22 | 20.55 | 19.1 | 18.5 | 17.92
Why the run ended
The experiment terminated when no further feasible complete route could be selected — not because of node death. All 44 sensor nodes remained alive at termination.
Lowest-energy nodes at termination: S3 (0.0000201 J), S2 (0.0000210 J), S1 (0.0000508 J).
9,189 is the round at which the routing table was exhausted of feasible paths — this is a route-availability limit, not a “first-node-death” lifetime metric.
M.Tech Reinforcement Learning • Q-Learning WSN Routing — Reconstruction & D0 Sensitivity
08
Notes: These are the headline results of the full 45-node experiment. The network completed 9,189 successful transmission rounds, delivering 4,704.77 Kbits of data while consuming just over 4 joules of total network energy, leaving about 17.92 joules of residual energy. All 44 sensor nodes were still alive at the end. I want to be precise about what 9,189 rounds actually means: this is not a first-node-death lifetime metric. The experiment stopped because the complete-path feasibility check could no longer find any usable route — some nodes, like S3, S2, and S1, were down to extremely small residual energy, on the order of tens of microjoules, but technically still alive. So the correct interpretation is that the network reached the point where its precomputed routing table ran out of energy-feasible complete paths.

## Slide 9
COMPARISON
Published vs. Reconstructed Results
Result | Lifetime (rounds) | Data (Kbits)
Published Q-learning | 6,260 | 3,205.12
Published Dijkstra | 2,737 | 1,401.34
Our Reconstructed Q-learning | 9,189 | 4,704.77
Chart: Completed Transmission Rounds
| Published Q-learning | Published Dijkstra | Reconstructed Q-learning
Rounds Completed | 6260 | 2737 | 9189
Chart: Total Conveyed Data (Kbits)
| Published Q-learning | Published Dijkstra | Reconstructed Q-learning
Data (Kbits) | 3205.12 | 1401.34 | 4704.77
Not claimed as an improvement
The higher round count and data volume are not interpreted as outperforming the original method. The exact topology, coordinate table, and several simulation parameters were unavailable and had to be reconstructed or assumed.
This indicates the reconstructed methodology behaves consistently with — but not numerically identically to — the reference method under the stated assumptions.
M.Tech Reinforcement Learning • Q-Learning WSN Routing — Reconstruction & D0 Sensitivity
09
Notes: This table and chart place my reconstructed result side by side with the two published numbers: the published Q-learning result of 6,260 rounds and 3,205.12 Kbits, and the published Dijkstra baseline of 2,737 rounds and 1,401.34 Kbits. My reconstruction completed 9,189 rounds and delivered 4,704.77 Kbits, shown in amber to distinguish it clearly from the published teal values. I want to be very careful about how I frame this comparison, though. Yes, my reconstruction completed more rounds and delivered more data than the published Q-learning result — but I am explicitly not claiming this as an improvement over the original method. As explained on Slide 5, my topology, coordinate seed, communication range, and D0 value were all reconstructed or assumed, so the two experiments are not run under identical conditions. The correct interpretation is that the reconstructed methodology behaves consistently with the reference method's qualitative behavior — Q-learning outperforming Dijkstra — even though the absolute numbers differ because of these necessary reconstruction assumptions.

## Slide 10
EXTENSION
D₀ Sensitivity Analysis
D₀ (m) | Rounds | Data (Kbits) | Energy (J) | Residual (J)
2 | 9,088 | 4,653.06 | 4.164968 | 17.835032
3 | 9,059 | 4,638.21 | 4.066465 | 17.933535
4 | 9,189 | 4,704.77 | 4.080833 | 17.919167
5 | 9,512 | 4,870.14 | 4.076632 | 17.923368
6 | 10,218 | 5,231.62 | 3.835497 | 18.164503
Amber row = frozen baseline (D₀ = 4 m) used in Slides 8–9.
Chart: D₀ vs Completed Rounds
| 2 | 3 | 4 | 5 | 6
Rounds | 9088 | 9059 | 9189 | 9512 | 10218
Chart: D₀ vs Conveyed Data (Kbits)
| 2 | 3 | 4 | 5 | 6
Data (Kbits) | 4653.056 | 4638.208 | 4704.768 | 4870.144 | 5231.616
Why this is the extension
D₀ governs when the propagation exponent switches from β=2 to β=4
Lifetime is non-monotonic: D₀=3 m gives fewer rounds than D₀=2 m
D₀=5 m and D₀=6 m yield progressively longer lifetimes
Goes beyond the frozen reconstruction — tests sensitivity to a key assumed parameter
M.Tech Reinforcement Learning • Q-Learning WSN Routing — Reconstruction & D0 Sensitivity
10
Notes: Beyond reproducing the frozen baseline, I extended the study by sweeping the propagation-distance threshold D0 from 2 to 6 metres, each run starting fresh from the same 0.5 joule per-node energy. The table and the two line charts show that D0 materially affects network lifetime, but not in a simple monotonic way: D0 equals 3 metres actually gives slightly fewer rounds than D0 equals 2 metres, while D0 equals 5 and 6 metres give progressively longer lifetimes, up to 10,218 rounds and 5,231.6 Kbits at D0 equals 6. This matters because D0 was one of my assumed parameters — the original paper doesn't state it explicitly — so this sensitivity study characterizes exactly how much that one assumption can shift the results, which is valuable context for interpreting the Slide 9 comparison.

## Slide 11
DEMONSTRATION LAYER
Streamlit Interactive Demonstration
■
3D WSN visualization
■
Source node selection
■
Route visualization
■
Route-level metrics
■
Final experiment results
■
D0 sensitivity results
⚠
S1 uses the recorded, audited route from the experiments. S2–S4 are feasible routing demonstrations on the reconstructed network and are not claimed as recorded Q-learning experimental selections.
The dashboard turns the notebook's static experiment outputs into an explorable, presentation-ready visual layer.
M.Tech Reinforcement Learning • Q-Learning WSN Routing — Reconstruction & D0 Sensitivity
11
Notes: To make the reconstruction tangible for a live audience, I also built a Streamlit dashboard as a visual demonstration layer on top of the notebook experiments. It renders the full 3D WSN, lets you pick a source sensor node, and visualizes the resulting route along with its metrics. It also surfaces the final 45-node experiment results and the D0 sensitivity results interactively, so a reviewer can explore the numbers rather than just read a static table. One important caveat I want to state clearly: S1's route in the dashboard uses the actual recorded, audited route from my experiments, while S2 through S4 are feasible routing demonstrations on the reconstructed network — they are shown to illustrate how the routing behaves, but they are not claimed to be recorded Q-learning experimental selections from the full run.

## Slide 12
CONCLUSION
Conclusion and Future Work
What was accomplished
Methodology reconstructed (reward, energy model, propagation model, Q-update)
45-node, 3D experiment completed — 9,189 rounds, 4,704.77 Kbits, 44/44 nodes alive
Energy feasibility incorporated with bounded, audited deductions
Results compared transparently against published Q-learning and Dijkstra values
D0 sensitivity extension performed (2–6 m)
Reproducible notebook and GitHub repository prepared
Streamlit demonstration dashboard developed
Future Work
More faithful reconstruction of original topology
Additional network configurations
More parameter sensitivity studies
Further validation across multiple random seeds
Thank You
Questions?
M.Tech Reinforcement Learning • Q-Learning WSN Routing — Reconstruction & D0 Sensitivity
12
Notes: To conclude: I set out to reconstruct the methodology of the Jrhilifa et al. Q-learning WSN routing paper, and I believe I've demonstrated that. I rebuilt the reward function, radio energy model, propagation model, and Q-value update; ran a full 45-node, 3D experiment that completed 9,189 rounds and delivered 4,704.77 Kbits while keeping all 44 nodes alive; incorporated careful energy-feasibility checks; compared my results transparently against the published Q-learning and Dijkstra numbers without overclaiming; extended the study with a D0 sensitivity analysis; and packaged everything in a reproducible notebook, GitHub repository, and an interactive Streamlit demo. For future work, I'd like to reconstruct the original topology more closely if that data becomes available, test additional network configurations, extend the parameter sensitivity analysis, and validate across multiple random seeds to check robustness. Thank you — I'm happy to take questions.